## Slide 1: Compressive sensing of audio signals
Physics 305 Activity 3
2nd Sem AY 2022-2023
Mark Jeremy G. Narag
2014-64423
PhD Physics

## Slide 2: All the codes and files in this activity are available on my Github: https://github.com/mgnarag/physics305_computational_imaging
A part of my code in this activity is from Cleve Moler of mathworks: https://www.mathworks.com/company/newsletters/articles/magic-reconstruction-compressed-sensing.html

## Slide 3: Compressive sensing
Background | Methods | Results and Discussion
Compressive sensing allows the efficient acquisition and reconstruction of signals, even when the number of measurements is much smaller than the traditional Nyquist-Shannon sampling rate!
Say for example that we let y be the random measurement
where C is the measurement matrix. We can express it as
where is our basis function (usually discrete cosine transform) and s is what we want to solve
subject to
where is the norm (Manhattan distance) given by
Equation from Ma’am Jing’s note on Compressive sensing

## Slide 4
Background | Methods | Results and Discussion
1. Create a note
It would be best to record a note from phone but I do not have musical instrument at hand so we will just create a note.
Let’s give note A a try where its frequency F is 440 Hz. We can construct it using
2. Pick random samples from signal, f
From the signal f, we pick b random 5% of our data:
Let’s also visualize the inverse discrete transform of signal f where we see spike at the appropriate frequency. This will be our basis later:

## Slide 5
Background | Methods | Results and Discussion
4. Find solution to Ax = b
To reconstruct the signal, we need to find the solution to Ax = b that minimizes the l1 norm of x.
In Matlab, we will use the l1-magic package written by Justin Romberg and Emmanuel Candès. Specifically, we will use the function l1eq_pd
5. Reconstruction
Finally, after getting x, we can reconstruct the signal by getting the DCT of x
3. Make it a linear system, Ax=b
The condensed signal is a vector b of m random samples of the original signal f. We construct a matrix A by extracting m rows from the n-by-n DCT matrix
A = D(k,:)
where k is the vector of indices used for the sample b. The resulting linear system is in the form Ax = b, with size m-by-n, which in our case is 410 by 8193.
There are 20 times as many unknowns as equations!
4.1 OPTIONAL: We can also opt to solve the traditional l2, or least squares, solution to Ax = b, computed by x = pinv(A)*b where pinv is a pseudoinverse that produces a matrix x of the same dimensions as A' so that A*X*A = A, X*A*X = X and A*X and X*A are Hermitian.

## Slide 6
Background | Methods | Results and Discussion
On top is x which is the l1 solution while on the bottom is the reconstructed signal f with only 5% sampling rate!
A_l1.wav
In comparison to the original:
PLAY IT HERE!
original
reconstructed

## Slide 7
Background | Methods | Results and Discussion
Additionally, let’s try the traditional l2 or least squares. We expect it to be noisy and not good (as can be seen from the reconstructed signal and the sound itself).
PLAY IT HERE!
original
Reconstructed using l1
Reconstructed using l2

## Slide 8
Background | Methods | Results and Discussion
But what if it is a complicated tone? Say for example the ”B” tone of a telephone. Here is the list of the frequencies:
So for “B” tone, it’s 770Hz and 1633Hz. Thus,
[9] Don Lancaster. "TV Typewriter Cookbook". (TV Typewriter). Section "400-Style (Touch-Tone) Modems". p. 177-178.
original
Reconstructed using l1
PLAY IT HERE!
Almost the same tune!!!

## Slide 9
Background | Methods | Results and Discussion
Now, let’s automate our code and try to play a song!
Ba-ba-black sheep/twinkle twinkle star has the note [A,A,E,E,Fbar,Fbar,E,E,D,D] where
A = 440; %Frequency of note A is 440 Hz
E = 659.26; %Frequency of note E
Fbar = 739.99; %Frequency of note F#
D= 587.33; %Frequency of note D
The reconstruction here is actually long…
original
Reconstructed using l1
PLAY BA BA BLACK SHEEP HERE!
YAY! Almost the same tune!!!

## Slide 10
Background | Methods | Results and Discussion
Conclusion:
We were able to reconstruct the audio using only 5% of the original data!
The downfall is that the reconstruction is actually very slow
Also, in Matlab, only few optimization function works. I had a problem installing some of the minimization packages like ConVeX (cvx) optimization package and CoSaMP - Compressed Sensing Matching Pursuit so I was thankful that I found the L1-magic package. It is actually not a built-in package. I found it deep down the internet forums :)
It would be nice to measure the difference – like PSNR on images.
Future works may include trying much lower sampling rate and applying a metric to judge the reconstructed sound.

## Slide 11
Reflection
I don’t do audio signals that much but this activity is very exciting! I can’t believe I did it I was actually scared to do this because it’s not an image anymore (weird to like 2D than 1D signal hehe).
CRITERIA | QUALIFICATIONS | SCORE
Technical correctness | Met all objectives. Theory is discussed sufficiently. Procedures and Results are complete. Procedures and Results are verifiably correct. Understood the lesson. | 40
Quality of presentation | All text and images are of good quality. Code has sufficient comments and guides. All plots are properly labeled and are visually understandable. The report is clear. | 30
Self-Reflection | Explained the validity of results. Discussed what went right or wrong in the activity. Justified the self-score. Acknowledged sources (e.g. persons consulted, references, etc.) | 30
Initiative | Experimented beyond what was required. Yes – I did l_2 minimization too Made significant improvements to existing code. Yes – automated a code that asks for several notes then outputs the compressed sound like the one I used in twinkle twinkle Analyzed limitations or potential of technique, etc. Yes | 10
100